AN217

CHANGING FRONT HOSES

If you own a 95, 96, or 97 and have not changed the brake hoses (front and rear), then it is probably time to do so.  Aside from developing cracks on the outside, they corrode and swell on the inside, eventually impeding the flow of brake fluid.  The symptoms of this may be dragging front brakes, uneven wear on the pads or excessive pressure required on the brake pedal to bleed the brakes.

As previously noted in the Newsletter, Beck-Arnley lists a replacement rear brake hoses for the V-4 (p/n 0730143) for $10.96.  Although the Saab Service Manual states that the front and rear hoses are of different lengths and must not be confuses, the Beck-Arnley hoses I bought for my wife's 97 are identical in every way to the Saab hoses I had previously bought for my '71 96.  The hoses are the same length front and rear.

If one orders the Beck-Arnley hoses, you must use the part number when ordering as they are listed by number only.  If you ask them for brake hoses for a 96 or 97 they will tell you that they have no listing for them.

How to change the front hoses:  First, clean the fittings thoroughly to remove any accumulation of gunk.  I use "Chemtool" to blast away the grease, and later clean and Armorall any rubber parts that may have been contaminated by the Chemtool.  Now remove the nut connecting the brake line to the brake hose.  This is accessible from the engine compartment.  Do not allow dirt or grease to contaminate the end of the brake line.

Now for the tricky part-unscrewing the lock nut on the brake hose.  This is accessible from the engine compartment.  Do not allow dirt or grease to contaminate the end of the brake line.

Now for the tricky part--unscrewing the lock nut on the brake hose.  This is accessible from the wheel well.  I assume that the car is now on jack stands with the front wheels off.  Use the box end of a 14mm wrench )the kind which has the box end slightly bent).  The box end can just be slipped concave side down over the nut.  The nut can be reached by passing the bent end of the wrench through the rear half of the access hole which is bisected by the brace supporting the brake hose.  After this nut has been removed, the hose can be unscrewed from the caliper.  Save the copper washer for the new hose.

Install the new hoses in reverse order.  The Saab Service Manual

recommends the following:

*Install hoses with wheels freely suspended and aligned straight ahead.

*When tightening the brake pope (line), hold the brake hose nipple (not the locking nut) to prevent the hose from twisting and changing position.

*Hoses must not come into contact with steering or suspension parts nor be twisted but be mounted in a neutral position.

*Front hoses should form a downward directed curve.

Above all, OBSERVE RULES OF CLEANLINESS WHEN WORKING ON BRAKES!