AN219

CARB WEBER

About a year ago, I replaced to FoMoCo carb (original equipment) on my Saab 96 V-4 with a Weber 34 ICH unit.  Performance seemed to be better, however, actual gas mileage did not improve noticeably and fuel fumes were always present after the engine was shut down in the garage.

Recently, my wife complained the car was operating poorly.  The engine would falter and stop while waiting at traffic signals.  Fearful of being unable to start again, she would accelerate excessively (race the engine) at stops.  Ultimately the engine balked and refused to start again.

Careful inspection disclosed that when cranking the engine an excessive amount of fuel was being forced through the carb orifices and accumulating in the carb body.  Raw gas was also abundant in the manifold.  The spark plugs were also wet and fouled and the engine oil on the dip stick was diluted with gas.

The above diagnosis invoked a thorough, premature tune up commencing with replacing the spark plugs and changing the oil and filter.  After further electrical work the Weber carb was removed, inspected and taken to foreign auto parts shop.  Here I was told that the float was operating properly and rested at the correct level.  I was informed that the Weber carb  is very sensitive and should be subject to gentle, low fuel pump pressure.  High pressure, say much above four pounds, the parts specialist cautioned, forces excessive gas through the float chamber and past the inlet needle valve.  So I measured the fuel pressure with a testing gauge and found it to be considerably above seven pounds!

At the specialist's suggestion, I purchased an adjustable fuel pressure regulator (a "Scat" VW high-performance item #35149 for $20.75).  This was mounted on top of the metal fan guard and directly in front of the carb fuel intake.  This regulator is presently set at four pounds pressure.

With a controlled amount of fuel entering the carb, I was able to get the engine started, however, only at a high rpm with the choke out and the accelerator depressed.  The engine would stop abruptly if either were relaxed.  I checked for air leaks, but all connections were fine.

In my desperation and frustration, I now studied with suspicion the solenoid idle device which protrudes from the right side of the Weber carb.  To remove, one needs a very small allen (hex key) wrench to back out a small black screw which secures the unit in place.  Next, remove the solenoid assembly by unscrewing with turns to the left.

Upon removal, one will discover four tiny pin holes-three in the circumference and one at the tip.  I cleaned the brass head and then tapped the unit in my hand and shook it which freed considerable trapped gasoline.  In the carb chamber vacated by the solenoid assembly by unscrewing with turns to the left.

A brief turn of the ignition key and--Eureka!  All systems were GO.  After warm up, minor adjustments of the carb throttle and mixture control produced a beautifully performing engine.  No strong gas vapor is evident now after shutdown.