AN222

CARB FOMOCO FLOAT VENT PROBLEM

Two quick tips to pass on regarding the '71 and later FOMOCO( carb for the V-4's. First, a frequent cause of carb (and sometimes engine) fires upon trying to start the car is the combination of a little back puff and a missing rubber bellows that connects the brass pipe on top of the carb to the bottom of the air cleaner (this is the float vent).

Second, another common problem is intermittent fuel failure causing bucking and jerking, or simply greatly reduced power on occasion, which is very aggravating. This is occasionally caused be a foreign object in the gas tank (usually rubber or plastic), but more often it is black flakes in the carb bowl. Where do these flakes come from? Paint flaking off of the air cleaner base and falling down the little rubber bellows into the bowl. To avoid this simply inspect the area around the small vent hole in the bottom of the air cleaner base, and scrape all loose paint and rust off the inside and outside, and clean the bellows.