AN224

FRONT WHEEL BEARING REPLACED

Almost all of the older 95/96 and 97 models still on the road are candidates for new front wheel bearings and seals. This can be accomplished without that heavy duty arbor press you've been meaning to buy. Removal of the old bearing can be accomplished by hammer blows as they are to be discarded. Protect the expensive machined parts with brass or aluminum stock, however.

The secret of reassembly is to deposit your shiny new bearing with lithium grease (not "wheel bearing grease"0 in your freezer for at least three hours. Heat the casting slightly with a propane torch and the frozen bearing will just about fall into place (number side out of course). Very light tapping will assure it is fully seated.

Now put the cleaned and re-lubed half shaft in the freezer. Being careful not to damage the seals, heat the inner bearing until the grease just begins to melt. Drop in the frozen shaft and tap the end slightly.