AN225

AUTOCROSSING SET-UP

I won the E-prepared autocross title for the third year here in Central Carolina Region of the SCCA. Next year I plan to do much more to the car. This year I did the following:

1. Weber 40 DFI carb

2. 3/4 race camshaft

3. MSS heads

4. Suspension lowered three inches

4. Braided steel brake lines

5. Full tube frame chassis built into stock pan

6. Lighten flywheel

Results:

1. The weber 28-36 DCD carb does not give as much top end as 	   the 40 DFI, though I would not use the 40 on the street due 	   to the poor mileage and cold starting.

2. The 3/4 race cam does not hurt torque and allows the engine 	   to rev freely.

3. MSS Heads offers several degrees of modification. The heads         I used have larger valves and porting. They are not the           super-trick dual port heads that Jack Lawrence uses on his         SCCA F-P Sonett. The porting and larger valves give much         better breathing and higher horsepower.

4. Suspension, right now it is as low as it goes and thats too         low for street use. Seven inch rear slicks now rub,               although the front tires do not. Handling is fantastic with          seven inch Goodyear slicks.

5. The stock SAAB brake lines flex and cause a loss of brake         pedal feel and power. My car now stops quicker and the            pedal feels stiffer.

6. A tube frame means between the front and rear suspension.         My roll cage/frame is SCCA legal and increases frame              strength. The car is much more predictable and is easier          to drive. At speeds over 120 mph, I also feel much more          safer. Sonetts have a very flexible chassis especially            between the front window pillar and rear bulkhead.                Improving the handling is limited by the chassis. Anyone          serious about fast driving should put in a full roll cage.

7. A lightened flywheel is worthwhile since it does not hurt         the low end and helps the trusty V-4 rev quicker.

AN225

Next year I plan to do the following:

1. Remove all street equipment, glass, heater, lights etc.

2. Dual port exhaust (MSS)

3. Dual Tilton brake master with separate masters for front         and rear.

4. Flared finders

5. Removable rear glass (lexan)

6. ATL fuel cell

7. Accusump

8. Coil over suspension

9. Oil cooler

10. Constant loss ignition

11. Removal of fan

This year the SCCA moved Sonetts from D stock to E stock, which will help them, but 99's and 900's were moved from H stock to G stock, which will hurt. But I think SAAB will still be competitive in autocrossing.