AN227

LEAKY DECEL DIAPHRAGM

I recently installed a rebuilt engine and carb (late Ford type). After going 200 miles the car started to sputter and die. After cooling for several minutes it would run fine. It would also idle without any problems until I pulled on the throttle. It would then start to die again. By enriching the air adjustment screw the car would run fine when hot, but poor when 10 minutes cold; when I leaned it out and started the procedure all over again. The diagnosis was a slight vacuum leak which would not appear in a vacuum test. Readjusting the float and checking for warpage also didn't help.

The problem turned out to be a leaky diaphragm in the decel valve. Since, in the past and this time too, I plugged up the decel valve, I never thought it could be a problem. However, there is an air hole at the bottom of the valve, which draws in air to the diaphragm, so even if disconnected, a leaky diaphragm will affect operation. The diaphragm costs only about $7.00 at SAAB or your Ford dealer. At Ford it is from a Pinto, P/N CM-2204.