AN229

TRANSMISSION REAR MOUNT

One thing that has always bugged me about my '69 Sonett was what appeared to be excessive movement of the gear shift whenever I'd be on and off the throttle, especially in fourth gear. I'd heard that the problem was a bad rear motor mount. I kept looking at mine but could see nothing wrong. Finally I tried it with my eyes open, and wonder of wonders, I did find something wrong.

1

The problem was not with the rubber in the center of the mount, but with that which is around the edges. The rear mount contains a large cupped washer. This washer helps prevent the engine from going too far forward when braking or when in an accident. It also, however, restricts the up and down movement of the rear of the transmission. When you accelerate, the transmission wants to move downward at the rear. This washer restricts the movement by pressing up against the rubber that is around the inner edge of the mount. On my car, this rubber was torn, allowing the washer ( and transmission) to move down farther than intended.

Since replacing the mount requires removal of the engine and transmission, I decided to try and repair the mount. I cut away the  torn portion of the rubber (about 1-1/2" long by 1/2" wide) using some exacto knives and a Dremel grinder ( the rubber is fairly hard and stubborn). I then replaced this section with a length of hard rubber of the appropriate thickness. For those wanting to do this repair, a possible source of hard rubber would be conveyor belting, which can often be obtained from farm supply stores. While you're at it, place a length of the rubber above the washer. This will help damp the upward movement of the rear of the transmission whenever you let off the throttle.

You can try gluing the rubber in place with contact cement, but if the rubber is stiff enough the glue may not hold. I held the rubber in place by adding a length of 1-1/2 x 1/8 strap iron (hardware store variety) between the cupped washer and the bolt that holds the transmission to the mount. I cut the strap iron long enough to extend beyond the washer, but short enough that I could still install that cardboard cover over the mount.