AN23

DON'T SLAM THAT HATCH

At least if you have a late '73 or '74 Sonett which incorporates hydraulic dampers. About mid way thru the '73 production year, SAAB shifted over to hydraulic dampers on the rear hatch. But then did not beef up the cast aluminum hinges and pins to take the additional stress and shearing forces which these dampers exert. Tremendous leverage is transmitted to the pins when you slam the hatch, and the soft aluminum pin will shear without warning if not treated very gently. Don't ask your friendly dealer for a replacement hinge assembly, would only give you heartburn.

Solution is to drill out the aluminum pins and replace it with a stainless steel clevis pin of suitable length, available at any nautical supply store. Insert and crimp the cotter pin which holds it in position, and hatch hinge is now better than new.

Dissimilar metals in direct contact sometimes deteriorate due to "galvanic" action, but stainless steel is relatively inert chemically, and in over a year I've notice no signs of corrosion in the aluminum housing surrounding the pin.