AN230

BRAKE OVERHAUL

I would like to thank everyone who as sent in tips to the Newsletter.  I think I've incorporated at least a score of tips into my current 96, from air filter modifications to a right-angle zerk fitting on my steering rack.  No tip i

s too small to send in.  For example, anyone who has been stranded (usually on a cold, rainy night, with no lights), due to those miserable old brass and porcelain Bosch fuses can appreciate the value of the tip about those pointy-ended stainless steel and glass fuses.  Also, my rear passenger window no longer leaks thanks to the neat fix for shrinking window gaskets.  And on and on.  Here are a few of my own tips and observations from the last couple of years.

Brakes: I am of the opinion that if an internal rubber component in your hydraulic system goes, you should seriously consider overhauling the whole system.  Let's face it, the newest of the 95's, 96', and 97's are ten years old, and their brake systems are best thought of as old inner tubes (i.e. at some point you give up patching them and you just replace it).  You can replace a cylinder here or a hose there, but the number of times you'll find yourself on your back bleeding fluid from your latest repair just isn't worth it.  In the recommended service interval section of Chiltons's Saab V-4 book, it tells you to replace all rubber components in the brake system every 36,000 miles--no joke!  Perhaps somebody out there with an official Saab shop manual could confirm this, but it's my bet that Chilton's got that piece of advice from Saab and didn't make it up on their own.  (Ed. Note:  The Owner's Manual for the 96 specifies that the fluid should be changed every 36,000, but says nothing about the seals.)  It may be that they were familiar with the track record of English-made components.

With the rear cylinders, replace them, don't rebuild them.  The good folks at Europa Motors in McHenry, IL warned me about this, but I ignored their advice, trying to save about $20 per cylinder.  Nine months later I was on my back replacing my rebuilt rear cylinder, and soon thereafter the one on the other side went too,  Apparently the dirt and sludge in the system settles at the lowest point, right where the rear cylinders are.  Once you do have the system right, bleed it once a year to keep that dirt out of those seals.

Parking brake link--That's the steel "L" shaped gizmo that connects directly to your hand brake cable right outside the rear drum.  The first time I took my rear brakes apart the thing was so rusted that I didn't realize it was supposed to pivot at the "crotch" of its L shape.  After you free it up coat the entire pivot point in grease so it doesn't seize again.  The reason it froze in the first place was probably because the nice little rubber boot that's

AN230

supposed to keep it dry was either shot, missing or mismounted.  This is the boot that covers the link right where it comes out the back of the backing plate.  Soak your new boots for a day or two in Armorall to keep them living longer.

When those boots are shot, or if you live in salt country, often times you will find that the rear brake shoe retaining pins, springs and cups are rusty or shot too.  I found a display in my local import parts emporium that had a set of these little gizmos that were almost exactly the same size as the Saab versions.  These are the pins, springs and cups that are referred to as "shoe steady" in the Haynes manual, page 132.

Suspension work in general--If you have the luxury of time, soak every nut and bolt in sight with penetrating oil for a few days in advance.  Note that all your suspension nuts and bolts are standard inch sizes on the 96, including the castle nuts on the axles.  You might find it cheaper and more worthwhile to purchase a great big adjustable crescent wrench than to get the individual 3/4" drive sockets and adaptors for the castle nuts.  An ordinary pulley puller of the correct size does the job of a wheel puller quite nicely.

If you have to pull a front axle for whatever reason grease--gun all the related zerk fittings (if your car has them) before you do the job.  If any of the rubber ball joint boots are cracked, they'll let you know with a nice big leak of grease.  Now is a good time to replace them.

When I installed my new Gabriel Red Ryder shocks on the front, I found that the rubber bushings they supplied were not long enough to compress properly by the retaining washer and nut, giving an almost loose fit.  Use a large U.S. washer, size 5/8" I.D. by 1 1/2" O.D., as a shim to give a nice tight fit.  Put your new "shim" on before putting on the bushing and shock.  One was enough for each mounting post.