AN235

HANDBRAKES

If you find that you can no longer get a firm lock with your handbrakes the cause might be worn shoes, stretched cables or worn drums. If your adjustment nut is all the way in on new shoes then the drums are suspect. To adjust the rear brakes, jack up the wheel and spin the tire by hand. Turn the adjuster nut until the brake locks and then back off till there is just a slight rubbing. if the cable needs adjustment be sure to adjust them with the handbrake off and the rear brakes adjusted. turn the two nuts on the cable (under the handbrake lever) until the brake holds on about the third click. Be sure to take a look at the rear axle bushings while down there.