AN238

HANDBRAKES

If cables, shoes/linings and drums are OK be sure to check the adjuster bolt and  "tappets" (the two little sliders that make contact with the shoes and adjuster, SAAB P/N 71-75-094). On my '73 95 both the adjuster bolt and the tappets were worn to a point where neither adequately nor accurate adjustments could be made. Replacement of these parts is easy and inexpensive.

While replacing these items be sure to coat them with anti-seize; it makes subsequent adjustments much easier. Brake cylinder bleed screws which have a light coat of anti-seize do not have the habit of rounding off or braking in the cylinders when turned open, even after several winters in salt/slush.