AN24

V-4 TRANSMISSION REWORK

Not long ago I overhauled the transmission because of mainshaft bearing failure. I would agree that it is always best to replace all suspect ball bearings, even if they look good. Usually this means mainshaft, countershaft, and clutch shaft (5 bearings). These are all very easily available from any halfway decent bearing dealer at less than half the dealers prices. I've been told that it is a good idea to replace the 4th gear needle bearing as it is frequently cause of failure. You'll have to get this at a SAAB dealer as it hasn't any reference number on it, and you'll also need an end cover gasket. It's been my experience that you don't need any special tools to overhaul a V-4 transmission provided that the pinion gear shaft doesn't need repair. I've had very good luck sealing the case halves, top and end cover with silicone gasket sealer (GE or NAPA) but you must be very careful to scrupulously clean the mating surfaces and then use a thin coat. Obviously you should always replace the driveshaft and clutch shaft seals. After trying 3 hours trying to reinstall the freewheel mechanism in its housing, I discovered that a large hose clamp works well in lieu of the SAAB special tool. As others have noted in this newsletter, the mainshaft and countershaft end nuts usually are loose, and should be loctited upon reassembly.

To my chagin, after installing the transmission and new clutch, the clutch wouldn't disengage completely, therefore wouldn't shift. The solution was to install a new (longer) clutch release bearing. Don't try shimming the clutch. As most of us know, its the same release bearing as old VW Beetles used.