AN245

WIPER REPAIR

After having trouble with my windshield wipers on my '73 Sonett, I pulled the motor unit out of the car and found that the brush plate was in need of replacement.  I found a replacement brush plate at local auto parts store, Lucas part # 54701528, cost about $23.

I also drilled two holes in the bottom of the motor housing, as suggested in the February 1979 Newsletter to prevent water from accumulating and freezing up the motor.  When drilling the holes care must be taken to prevent a small round disc from falling out of the housing.  This disc is in the center of the housing bottom, and is the plate that the motor shaft rests on.  I lost mine when it fell to the ground (I was working on it outside).  I had to make my own and guess at the thickness.