AN246

FLYWHEEL BOLTS ALTERNATIVES

It seems that I spend quite a bit of my time trying to find lower cost (not cheaper) parts for Saab automobiles.  A case in point is the flywheel bolts for the V4 engine.  Ford/Saab tells us to torque these bolts to 50 ft lbs, which is a stretch torque figure, and then when we pull the bolts at some later date (as when we have to change a rear crankshaft seal or have the flywheel surfaced) we remove the bolts and throw them away.  Good idea to discard them, because they will probably break the next time you use them since you already stretched them once, remember?

Saab charges around $2 a bolt for these beauties and that means you get swacked for at least $12 just for taking off the dumb flywheel!  There must be a better way.

Some research at the local House of Henry produced a more palatable solution.  The flywheel bolt used on the Ford Mustang V6 AND the Pinto just happen to be the same pitch thread and the same diameter (10 mm) and though they are a couple of mm longer, they work just fine and clear the input transmission shaft and the clutch plate AND even hold the flywheel on good.  You will have to use a 17mm socket instead of a 16mm socket to tighten them up.  Use Saab's 50 ft lb torque figure, of course.  Price?  About 95 cents each, retail, a considerable saving over the cost of the Saab item.  FoMoCo Part Number is D4FZ-6379A.