AN249

FREE-WHEEL TOOL FABRICATED

While reassembling the transmission on my 96 DeLuxe I had great difficulty getting the 10-roller freewheel back together.  Trying to hold all the parts in place and install it into the primary shaft seemed impossible.  So I made a simple and cheap too, which works great.

The tool shown in the plans was made for a 10-roller freewheel; if you want to use it for a six-roller unit, the hole in the side must be enlarged to accept the larger rollers.  If used properly a freewheel can be assembled in approximately 10 minutes.  Also, once the freewheel is assembled in the tool it can be pushed directly into the primary shaft.