AN25

CARE FOR SONETT WINDSHIELD REFECTIONS

If your over 5'-10" and drive a Sonett at night you are probably irritated by the instrument lights reflecting off of the windshield right at the eye level. Solution:

: 1. Disconnect speedo cable at transmission.

: 2. Remove 4 screws holding instrument cluster inset.

: 3. Push speedo cable in from hood (or pull on panel) and pull          instrument cluster back into car.

: 4. Be gentle with speedo connection to speedometer. Mine was         made of a plastic and shattered when I attempted to put it         back on. I recommend not disconnecting it in the first            place, as sufficient slack is guaranteed by Step 1.

: 5. Remove tach from cluster (label the wires)

: 6. Remove small plastic recepticale from back of tack where         wires connect. This exposes a small square hole.

: 7. Use a small "artist" paintbrush that fits through the hole         and paint over the existing reflective silver finish. Be         careful to get the paint only where you want it. Make sure         to cost silver edge visible from front of tach just behind         glass.

: 8. When the paint has dried, reassemble everything.