AN252

SONETT BRAKE LINE REPLACEMENT

After a panic stop something was amiss with my Sonett's brakes.  Pumping would produce some braking action, but steady pressure resulted in that awful sinking feeling.  After a careful retreat home I checked the following for leaks: wheel cylinders, exposed brake lines, and mad cylinder pushrod boot.  These were all OK but since the reservoir level was going down I knew it had to be going somewhere.

After pulling up the carpets and floorboards I found a half inch of brake fluid puddled in the groove carrying the two rear lines.  Pushing the pedal brought up a geyser from a rotten area in the right line near the accelerator pedal. From past experience I knew that new lines could be bought as standard 3/16 bubble flare without difficulty, so I was not too worried.  Even so, the prospect of running a new line through all those bulkheads looked like an all day job.  I figured there had to be an easier way out.

I wondered about those copper line compression fittings.  Consultation with a few friends resulted in the consensus that the fittings were ok if the lines were steel.  So off to the hardware store for four 3/16 compression couplings, eight nuts and eight ferrules.  Then to the 96 hulk for two feet of clean brake line.

I replaced the corroded area in both lines, using steel wool to clean them before cutting and a little silicone grease on the threads.  It works fine, and only took about an hour and under $5.00 cost.