AN253

SONETT HOSES PVC AND THERMOSTAT

In response to "Sonett Cooling System Hoses Misrouted" there is no need to reuse the original small molded heater hose that connects to the heater thermostat valve.  Most auto parts stores stock 90 degree molded heater hoses. similar to the one used on the  Sonett.  The only difference being the longer length of the hose which is no problem to trim down to match the original hose.  I had good luck with finding this hose at a NAPA parts store.

Also, if you plan to replace all of the cooling system hoses on a 1973 Sonett III (I am not familiar with the other years), also replace the screw on the top of the rectangular "block" that the PVS (positive vacuum supply) valve screws into.  Anyway, this particular screw on my Sonett was half eaten by corrosion.  I found a replacement at a foreign motorcycle shop and made the washer for it out of gasket material.  I suggest soaking this screw with penetrating oil before attempting to get it out of the "block."

PVS Valve--If you want to keep the distributor advance system stock and are in need of replacing the PVS valve, you can get one from Ford for about $30.  The part number is DY-165-1, D7AZ-12A091-A.  The identification numbers on the original part cross reference in the Ford parts catalog.  This valve assembly was used in some 1973 Mercurys.  The new valve is partly constructed of plastic rather than being cast.

Does this type of advance system have any beneficial effects?  Especially if you put a 160 degree thermostat in the car, since the PVS works off of the water temp.

Thermostat--I recently purchased a 160 degree F thermostat for my Sonett from Ford Industrial.  The part number is C5JZ 8575B.  The cost was a bit high at $12 where I purchased it.

Ed. Note:  The Factory Sonett manual describes the operation of the PVS as follows:  "When the temperature of the coolant is  raised (sic) above +225 degrees F (107 degrees C) the valve readjusts the vacuum advance so that the idling will be faster and the engine cooling will be improved."