AN257

SWAY BARS SONETT

Yes, sway bars do indeed exist.  Most owners have seen the front model that Saab installed until sometime during '73 on 95's and 96's.  At that point they were dropped from the car.  But they can be found in junkyards, Newsletter classifieds, etc.  The 96 front sway bar also fits Sonetts.

To install on a Sonett it is easiest when the engine is out of the car.  It is possible with the engine in,but it requires removing the starter, and exhaust, and gently jacking the engine up and inserting the sway bar from the side.

With the engine out, look for the large hole inside the engine compartment left and right that is plugged.  It will be necessary to remove the plug.  Above the large hold on each side are a pair of smaller holes that may or may not be blocked by metal.  Drill these out as they are for the rubber bushing brackets.

Remove the two bolts on the lower ends of the A-arms and install the rubber bushings and sway bar as one by replacing the bolts.

The above also applied to 95's and 96's lacking front sway bars.

All this becomes even more important if deciding to install a rear sway bar.  They are available from ADDCO (Lake Park, FL  33403, 305-844-2531).  On the Sonett a rear bar may be too much to handle and just plain unneeded.  However, on the taller 95 it is a nice bonus.  The rear bar attaches by means of an "L" bracket to the lower shock mount, replacing the shock washer.  The bar itself leads forward and attaches to the floor via a rubber bushing and metal brackets.

In 95's you will have to use four bolts with washers to install, as the enclosed U-shaped bolt will not fit.  The holes are both sides of the bulkhead behind the spare tire.

The difference is well worth the time and effort.  The lean is not the monster it once was.  And with a set of P-8's or maybe oven P-6's.