AN261

SWAY BARS INSTALLATION

Regarding the addition of a front stabilizer (sway bar) to a 72 or later 96, Saab re-routed the metal fuel line running through the engine compartment when they did away with the bar.  If you add the bar with the engine out you will see that the bar can run through this line and eventually cause a leak and fire.  If you add the bar with the engine in you won't notice this at all, as was my case until a transmission exchange uncovered the potential for disaster.  My metal fuel line was more than half way worn through.  Routing the fuel line as in a pre-1972 92 solved the problem.