AN265

HOSES AND FLUIDS

In regards to Peter McLaughlin's brakes (or anyone else's 96 brakes for that matter) as a mechanic I have twice run into situations where the flexible hoses to the front calipers have swelled internally (wrong brake fluid)?  leaving enough of a passage for fluid under pressure to get to the brakes, but fluid at the brakes does not have enough pressure to squeeze back through the restricted passage, causing massive brake drag which heats everything up, which causes more drag, etc.  I would recommend that anyone with a front drag problem should jack up the front of the car, select neutral, and have an assistant push the pedal hard and release while you try to spin the wheels by hand.  The wheels should be free to turn almost instantly upon release of the brake.  If not, remove the wheels, loosen the bleeder fully, and push the pistons back with a suitable tool.  If they move freely, with fluid squirting from the bleeder, and there is no mechanical problem (rusted caliper pivot, slide points, etc.) I would suspect the hose.

One side at a time, undo the hose at the caliper, put the loose end into a contained to prevent a mess, and watch the hose as the faithful assistant again presses the pedal (not so hard this time).  If the hose is blocked, the fluid will dribble from the hose instead of spurting out, and the pedal will give a definite resistance instead of going straight to the floor.  For a final confirmation, you can remove the nose (a handy thing to do since you want to replace it anyway) and blow through it.

In both cases I ran across, only one side had gone bad, but if I found one bad I would replace both of them if possible, and flush the system with correct fluid.

By the way, I recently rebuilt the brakes on my 122 Volvo, and refilled the system with silicon fluid.  About a week later, I began having problems with the pedal not returning.  On disassembling the master cylinder, I found little bits of crud blocking the hold that allows fluid from the reservoir into the cylinder itself.  Apparently I had left a little bit of conventional fluid in the reservoir and it had "curdled" and formed lumps.  Once I had cleaner everything out and refilled the cylinder again, it worked fine.  I have 2 other cars running silicon and have had no problems, but the both started from scratch with new brake systems.  If you are going to use silicon, make sure you get all the old fluid out before the silicon goes in.