AN266

CLEANING DURING REBUILDING

Seems to me that cleaning up the parts during a repair job takes about as long as the repair, and it just about as important.  Gasket scraping is a real pain.  Well, don't despair!  An old product comes to the rescue!  JASCO makes a "Paint and Epoxy Remover" that you can brush on cantankerous gaskets and just sit back and let chemistry do its thing for you.  In about 10 minutes either all or most of the gasket will just wipe off with a paper towel.  A second application of the stuff will remove what didn't  come off the first time.  It works good on even the toughest gaskets like the ones on the timing covers of Saab engines, end cover gaskets on V-4 gearboxes, etc.  You don't have to worry and more about damaging aluminum surfaces that are machined to close tolerances because of scraping off old gaskets.  Don't sweat it--JASCO it!  About $3.50 for a 16 oz. can.  Try it--you'll like it!

For those who do their own engine overhauls, cleaning up the piston ring grooves can be a bloody pain, too.  A lot of careful scrapping with half an old piston ring is the proper way to do it, but its still a lot of work.  If you will remove the old rings and then soak the pistons over night in mineral spirits, paint thinner, or diesel fuel, you'll find that most of the build up in the groove will just push off the surface the next morning.  Your clean up time per piston will be about a third what it would be otherwise!