AN271

FLYWHEEL BOLTS

The guy in Peoria didn't change his flywheel bolts.  He drove it for a long time and nothing happened.  So what's the big deal about changing these bolts, anyhow?  Well, if you read the Saab Service Manual you will discover that in the Ford/Saab V-4 engine there are 2 sets of bolts that MUST be replaced ANY TIME they have once been torqued and then unscrewed.

The reason is in the torque figures.  The flywheel bolts are torqued to 50 foot pounds.  The rod bolts, the other replaceable bolt in the V-4, is torqued to 24 foot pounds.  Both are just about 15% beyond the normal torque range for a bolt of that grade and that diameter.  In fact, they "TORQUED TO STRETCH".  They DON'T come loose, either, though neither uses lock washers of any kind.  It's an old Ford trick that works well, but does cause you to have to change them when you unscrew them.

If you DON'T change them, there is a very good chance you will snap them off the next time they are torqued up to spec.  If the guy in Peoria had ever seen the inside of a V-4 bell housing where the flywheel came loose--especially at about 6000 rpm--AKKK!  The price of a set of bolts is really CHEAP compared to fixing up that mess!

Happily, no such condition exists (torque-to-stretch) in the 99 or 900 engines.  The V-4 is a Ford engine and thats how Ford did things when that engine was designed.