AN275

ACCESS TO ENGINE COMPARTMENT

Much has been written about the 97-III's hood and its removal and replacement. However I'd like to add my 7 cents with some comments gained from experience on two 97's my sons own. The hood attachment points at the stay attachment to the bumper require a gifted double-jointed orangutan to remove. And an octopus with eyeballs on half of his tentacles to install these bolts and nuts. If you spot weld the nuts in place when you have the hood removed you can get out of the zoo business.

Before welding, observe the relative position of the nuts/bolts (inside or outside the frame). It might make a difference around the radiator bolts. Be careful of the fuel line near the left front bolt.

Before putting the hood back on:

-Always remove and check the wiper motor.

-Examine, critically, the brake and clutch master cylinders. With the hood on, you better get your zoo partners back. In fact, I think I'd rather remove the hood to replace the brake master cylinder than to do it as suggested in the manual. In this regard, I've considered putting a piano-hinged access door in the left wheel well to get to both master cylinders.

-Degrease and clean the engine compartment and remark the 0 DEG position and timing points.

-Of course, check all lines (fuel, water electric) and fix if needed.

And just before you put the hood back on:

-Check the alignment of the speed nuts (6 of them, three on each door pillar) to be sure your screws will mesh. Secure them in place.

-Remind yourself to put the arm of the headlight mechanism into the support bracket as you install the hood. (It can be disassembled on an installed hood if out of the slot, reposition into the slot and reassemble.