AN276

SONETT GEAR SHIFT LINKAGE

Various components of the gear selector linkage wear, causing slop at the gear selector and, in extreme cases, difficulty in shifting, especially downshifting to second gear. These appear to be two major problem areas. The first and simplest to fix involves the linkage U-Joints. There are two joints located directly under the shift linkage console. To check these, remove them from the car and place one end of each U-Joint in a vise, hold the other end with a large pliers, twist radially. If there is any significant movement, this indicates wear. It is difficult to attempt this by hand, since a larger force is required to detect wear.

The second problem area is considered more difficult to attend to. At the point where the shift linkage meets the transmission, it passes through a bushing in a bracket mounted to the transmission. This bushing wears and is very difficult to see and therefore can go undetected. The major obstacles to replacing this bushing are: unless you are very imaginative, it is nearly impossible to replace in the car (although where there is a will, there is a way), and the bushing is not available as a spare part from SAAB. This bearing is made from a material called oilite and must be purchased from a bearing company and adapted.