AN28

BALANCE SHAFT FAILURE

Most V-4 owners know that their engine was built by Ford in Germany. It has proven to be a most rugged and reliable power plant. There is one failure that occurs rarely, however, that requires major labor to repair. That is the loss of teeth from the balance shaft gear.

The crankcase has a steel gear on the end of it. This gear drives the cam gear, and a fiber gear on the balance shaft. It is the end of the balance shaft that comes out through the "transmission cover" and has the pulley that turns the water pump, fan and alternator. The stop-start load of the air conditioner compressor can cause failure of the balance shaft fiber gear, but I recently lost one on a '73, never air conditioned, at 53,000 miles. The indication (while driving) that it failed, came when the alternator light came on when the heat indicator went to "hot". The indication under the hood was that the fan belt turned easily with the engine shut off. If only a few teeth have sheared off, the belt may go back and forth a bit, but you will know that it is unusual.

The usual repair is to remove the engine, remove the pan, change the gear, and reassemble and reinstall. I tried a short cut and it worked well for me. I used a "Sawzall" to cut two cuts about 4" long down the front of the oil pan after the radiator and transmission cover was removed. The old gear was then pried off, the flap of the oil pan being sprung forward in the process. The new gear (and I used the steel replacement) was installed, and the slots welded. I could not weld a short piece of the slot under the lip of the pan, so I cleaned it thoroughly and covered it with RTV rubber, inside and out. One Caution: make sure the balance shaft spins freely, as bits of the old gear may bind it tightly. If this occurs, engine removal is mandatory.

This is not a SAAB approved repair, but it worked for me and saved me a lot of man hours. If you lose the balance shaft gear and need to replace it, it is worth your consideration.