AN280

MORE HELP FOR V-4 OWNERS

My 1969 96 V-4 just passed the 180,000 mile mark and continues to run like new. It has been a remarkably inexpensive car to operate.

For those V-4 owners who start to detect a growling noise in 4th gear at from 45-55 mph, you'd better get the car to a shop and consider a transmission rebuild immediately. The noise on mine gradually got louder over 10,000 miles of driving, and I thought that I was hearing bearing noise.The transmission had not been rebuilt since new and had 178,000 miles on it. The teardown revealed that the main shaft nut had done nothing more than lost its torque, but that was enough to put a new wear pattern on the ring and pinion. The mechanic told me before the rebuild that, unless the ring and pinion were replaced, the noise was going to be there after the rebuild. He said that he could only shim parts on the shaft in order to put the noise at a speed that would cause less disturbance in everyday driving, and that was the way things turned out. Even with the extreme mileage on the transmission, the freewheel hub and clutch were OK, and there was very little internal wear. If the shaft nut had not come loose, I could of gone another 50,000 miles on the transmission. I've used moly in the gearbox for about 80,000 miles, and it obviously does the job.

Also, for those of you that are using the 43mm carb sold buy SAAB Motor Sport, long highway runs in hot weather will cause engine heat to be transmitted from the manifold to the carb, thus causing fuel to heat up in the float bowl, atomize, and then percolate from the carb. The car runs richer, and the idle deteriorates. A thicker gasket needs to be installed between the carb and manifold to prevent this.

I have used Key oils and lubricants in my 96 for over 100,000 miles, and I couldn't rave enough about their effectiveness. Their motor oil is good for a 10-15% increase in gasoline mileage, and if engine and transmission wear are true indicators, friction must be reduced dramatically. Their lubricants are highly refined and also use Jojoba bean oil. Send to the following address for brochures, price lists:

Key Oils and Lubricants

8202 Allport Ave.

Santa Fe Springs, Ca. 90670