AN285

BALANCE SHAFT REPLACEMENT

I recently replaced the balance shaft gear with the engine in the car. Just a couple of tips: Remove the alternator belt, fan radiator, timing cover, etc., to expose the gear. Remove the oil pan bolts you can get to easily. Pry down gently on the oil pan just enough to remove the gear. Make sure you clean out the oil pan full of old teeth before you install the new gear. Use a spring loaded grabbing tool for the big pcs. and rinse the small pcs. out the drain hole. Also be sure to get the timing marks on the gears lined up properly. Install the new (used?) gear the same way, with just a little more prying. Be careful not to slip and get your fingers caught in the process, and don't pry so hard the oil pan bends. Clean the mating surfaces and install the oil pan and timing cover with a good quality silicone sealer. Reassemble the rest and your back on the road.