AN287R

THE "OTHER" BEARINGS IN A V-4

In the November '86 NINES "Tech Talk", Mr. Bartlett recounts a method of V-4 balance shaft replacement.  He also mentions going through old Saab Club News issues before tackling a task, something I have done a lot.  As a writer of some old SCN articles, I now find myself in the slightly uncomfortable position of being older and perhaps wiser than when I wrote them.  An "extended mileage report" on my old tips has often been started, but it never quite makes it as far as the mail box.  Belated thanks to Mr. Bartlett for jarring my sense of responsibility about this matter.

Those of you with a collection of old SCN issues please make a note in the May '84 SCN on my article on page 5.  The note should refer you to this issue of NINES.  That old article suggested the possibility of creating an "access panel" on the front of the oil pan, for the purpose of quick and easy roadside balance shaft (b.s.) gear replacement.  Nice idea (it would do the trick), but, like Mr. Bartlett's repair, it overlooks a major cause of phenolic b.s. gear failure and that is worn b.s. bearings.  (Phenolic is the name of a plastic or resin compound used in making the gear.  Saab also offered an iron gear to be installed on air-conditioned 95/6/7/s.)  When the bearings get very worn they cause radial play (wobble) in the shaft, and the phenolic gear can then "hit" against the iron crankshaft timing gear, eventually shredding the teeth off the b.s. gear.  I don't have enough information to say that this is the only cause of b.s. gear failure.  I would say that in high-mileage V-4s that have had unknown oil change intervals (i.e. multiple owner used cars), the likelihood of the bearings being at fault is very high.  That guess is based on my own experience and years of talking with other 96 dinosaurs.  After my latest b.s. gear failure, I bought a new iron gear from Motor Sport Service, and all the attendant gaskets, seal, etc; figuring it would be a one day job at most.  Then I removed the oil pan.  Amongst the expected chunks of b.s. gear teeth I found large and small pieces of what turned out to be bearing material.  It was a little thicker then duct tape, like lead foil.  (So much for the day).  Surprisingly, it was the rear bearing that had fallen apart; the front bearing, which is the more usual culprit, was still intact.  Bearing replacement meant pulling the shaft, which means pulling the flywheel, which means most definitely pulling the engine.  (I took advantage of my misfortune to do a clutch job, pilot bushing, input shaft seal, etc.)

What are the caused of b.s. bearing failure?  First, the b.s. bearings are pretty much at the end of the line, oil pressure wise.  In a new, tight engine they do just find.  But with age and wear, tolerances on all the engine's bearing surfaces begin to open up. and oil pressure drops off.  It's like holding your thumb over the end of a garden hose.  Squeeze down tight and you get high

AN287R

1

pressure; loosen it up and you have a dribble.  Second, the oil pump is wearing right along with everything else, putting the b.s. bearings in further jeopardy.  Third, we're not dealing with a bunch of spring chickens, and they may have been subject to chicken abuse, i.e. infrequent oil changes.  Dirt in the oil is an abrasive.  Babbitt-type shell bearings are relatively soft:  it doesn't take much abrasive at 1-6,000 rpm  to wear them away.  Just think of a belt sander in your engine the next time you hesitate to change your oil.  T.L.C. may be why some b.s. gears soldier on for 150,000 miles, while others crap out as early as 60 yo 80,000.  Other factors such as driving style come in to play, but none are as deadly as dirty oil.

Replacing the phenolic gear with an iron one might seem to be the answer to all your b.s. problems.  In the short run, absolutely.  Iron gears do compensate for hard acceleration as well as the load imposed by air conditioning compressors.  I'm sorry to report that neither Saab nor Ford Industrial carry the iron gear any longer.  Saab recently substituted a nylon gear for "heavy duty service" applications.  The good news is that it costs about half the price of an iron gear.  Ford does offer oversize b.s. bearings, something Saab never did.  The logic is that on an industrial engine with an iron gear, the darn thing will continue working after the bearings have gone away, thus damaging the shaft.  THis would call for grinding the shaft bearing surfaces, just like you'd do with a crankshaft.  Depending on your point of view, the oversized bearings are either enlightened foresight or the fix of an additional problem created by the iron gear (coupled with abuse).

Hardest to substantiate is the dynamic of phenolic gear failure itself, exclusive of bearing failure.  I have an article on phenolic camshaft gear failure on Model T engines.  (Seems Ford has been fond of this material for a long time.)  The author suggested that the phenolic material does not do will in extended storage, and may be subject to water-freeze damage.  Incidentally, the Model T fix rings familiar; they recommend replacing it with a metal gear.  Phenolic gears are subject to the same wear as everything else in the engine. When they get worn, the backlash of your timing gear set gets too wide.  This may allow the iron crank gear enough room to get a running start at the relatively weaker old b.s. gear.  Or it may set up vibrations that spell failure.  In either case,

AN287R

checking the backlash of the whole gear-sets is a worthwhile thing to do when you have the front of the engine opened for whatever reason.

The moral of this article is that replacing a b.s. gear without looking at your b.s. bearings is asking for trouble.  A sub-moral might be that a V-4 that eats its b.s. gear may very well be an engine asking for a bottom-end rebuild, or at least inspection.  With the oil pan out of the way, you have access to the connecting

rod and main bearings, as well as the oil pump.  If the engine still has good compression, attention to some or all of the aforementioned items might extend its life considerably.

Diagnosis:  Occasionally, on a V-4 with a really shot front b.s. bearing, you can grab the b.s. pulley and feel or see radial play in it when you push/pull it side-to-side.  Do this with the fan belt off. Try not to confuse radial play with backlash (rotational); even a new engine has a certain specified amount of backlash in the timing set.  It was a suspicious noise that brought you to this point, it could be a bad front fan bearing.  Spin and wobble it too to see if it may be at fault.  (The fan bearing is another item you may wish to change when you have the timing cover off the engine.)  Unfortunately, if the rear b.s. bearing is bad, the play probably won't be perceptible.  Since we're speaking of bearing running clearances, another caveat is that we are in the realm of thousandths of an inch.  A b.s. bearing could be within a gnat's ass of failure, and your hand/eye may well not see it.  One of the best bottom-end diagnostic tools is an oil-pressure gauge.  I've been running around with one of these things hanging off the bottom of various 96 dashboards for 15 years, and I think it's finally going to pay for the initial 8 dollar investment.  (This is a mechanical gauge, vs. the electric type.) When my recent (Jan. of '86) b.s. gear failed, it was on my wife's "new" 95, and with just an idiot light, the only warning it gave was its death.  Presently on my 96 with the gauge, I have lousy oil pressure at idle, a new development.  Given the otherwise good health of the engine, I suspect b.b. bearing trouble.  A C.O.D. order to M.S.S. produced a new nylon gear, new iron oil pump (unlike the O.E.M. variety, which is aluminum bodies and in theory less wear resistant), and a set of connecting rod bearings, which Jack Lawrence said are also at an end of the oil-pressure line, and are suspect.  The moment I discover the exact nature of the problem, I'll report it.  Another diagnostic trick is to "analyze" your old engine oil by running it through an automobile paint filter.  These are cheap paper filters with fine mesh screens built in.  You also might want to take a long skinny (magnetic) probe and pull what you can off the bottom of your oil (drain) pan after you've drained it.  Via both methods I discovered tiny little pieces of bearing babbitt in the oil and on the bottom of the oil pan.

AN287R

One final note:  Replacing the b.s. bearings can be done with ordinary hand tools if you're careful and sensitive to this kind of work. Basically, you use the balance shaft itself as a guide/arbor to do the job.  Normally, one would have them replaced along with cam bearings at rebuild time.  I imagine the machinist would use the same or similar tools for the b.s. as the cam bearings.  This would be done after the block was hot-tanked, as the chemicals used for cleaning destroy bearings.  A word of caution, there is a trough on each b.s. bearing.  Make certain the trough is pointing the right way and the oil hole in the bearing lines up with the oil passages in the block.  Good luck to you.