AN29

CLUTCH WON'T RELEASE

For no apparent reason the clutch on my 1970 96 started to have trouble releasing. The pressure plate, disc and throw out bearing had all been replaced within the last 10,000-20,000 moles. I adjusted the clutch play to its minimum and checked to see that the hydraulic components were working properly, but still the clutch pedal would engage about 1/8" above the floor, and with the engine running and the car stopped it became difficult if not impossible to shift into any gear. This difficulty was not experienced with the car moving, nor was there any difficulty shifting without the clutch in freewheel.

So I took the car and checkbook to a SAAB dealer anticipating an expensive clutch overhaul or transmission work. The agreement was something was wrong probably a weak pressure plate, but couldn't tell for sure without the whole thing taken apart. The dealer tried an alternative solution. He shimmed the hydraulic slave cylinder, that is he loosened the bolt holding the slave to the transmission case and slipped a couple of washers in between the cylinder and the case, moving the cylinder forward enough to allow the pressure plate to release more completely. This amazingly simple solution cured my problem completely.

A WORD OF CAUTION: After shimming the clutch start the engine with your foot OFF the clutch pedal and push it slowly and carefully toward the floor to be sure that the throw out bearing lever does not touch the spinning pressure plate with its new extended range (click-click-click). If it does, back off or forget it. If not drive away.