AN291

DON'T OVER TIGHTEN FAN BELTS

As an experienced mechanic on V-4 models, I found the last article in NINES on balance shaft bearing failure to be a good one. I agree that T.L.C. is why some bearing shaft gears and bearings last 150,000 miles and the article covered the bases very well except for one point: Don't over tighten the fan belt!

I and many others have written in the past to remark that water pumps on V-4's should last over 100,000 miles, not 25,000 moles as some owners report. My experience with dozens of cars has shown that replacement intervals on water pump bearings, fan bearings and alternator bearings is a direct relationship to the mechanics adherence to the SAAB Manual recommendation of 7mm play in the belt! Too often a new customer has come to me with an over tightened belt and a noisy water pump. This general observance and theory can also be applied to the balance shaft bearing, although lubrication can allow the bearing to hold its own as long as clean and good oil flow exists. With nearly 200,000 miles on my original balance shaft bearings (new gear installed a few years ago) in my 1971 95 V-4 I'll keep my belt where it is.

By the way, a tell-tale sign of a bad front balance shaft bearing is an oily film all over the inside of the hood and fenders in the engine compartment. This is due to uneven travel of the shaft within the front cover (pulley) seal. Oil shoots/leaks out around the shaft and the fan distributes all over the engine compartment and front cover.

Don't neglect the oil pump when the pan is off. Even if the oil pump is good, never remove the pan without checking and changing the six sided "oil control rod" which drives the oil pump off the distributor. This $7.00 part is well worth changing. Check the receptacles for the rod in the oil pump as well as the distributor for excessive "rounding of corners". This wear is consistent for every SAAB V-4 with over 100,000 miles I've dismantled, and if not corrected, oil starvation will result as some point.

While I'm discussing parts for under $10.00 that can prevent major bills, I hope anyone that has a deceleration (FOMOCO) valve still in the V-4 carburation system has replaced the diaphragm or checked underneath the base of the housing for an air leak while the car is running. If there is suction from underneath, the rubber diaphragm has an air leak disrupting the fuel-air mixture, causing a #1 or #4 cylinder exhaust valve to burn. And a good valve job (with unleaded gas type valve seats) is no longer cheap on the V-4.