AN293

UPDATE ON BALANCE SHAFT BEARINGS

In the January NINES article on balance shaft bearing problems I promised a report on what was found when I tore down my 96 engine.  As you may recall, I was discussing b.s. bearing failure diagnostic measures, and suggested that a mechanical oil pressure gauge was one of the best methods around.  During September the 96 oil pressure became lousy at idle, and in the next oil change I pulled bearing babbit material off the bottom of the oil pan (sump).  On the hunch that both nasty developments signaled the failure of the b.s. bearings, I immediately purchased a new nylon b.s. gear, bearings, seal, etc.  I finally freed up my garage this week and pulled the engine.  Bingo!  BOTH b.s. bearings had lost ALL their soft inner layer of babbit material.  The bottom of the oil pan was completely strewn with flakes and chunks of it.  Thanks to the oil pressure gauge, I managed to nurse the 96 along (around town trips ONLY) for five months by placing an egg between my foot and the accelerator pedal.  (Both my previous b.s. gear failures had occurred under normal but hard acceleration.)

I would NOT recommend anyone nurse an ailing engine as long as I did, but I had not choice.  A word of praise to the humble but vigilant NAPA oil pressure gauge.  Thanks to that little 12 year old item I was able to PLAN the repair, but the parts IN ADVANCE, and CHOOSE the time to do the repair.  Plus I avoided all trips that put me into the megabuck towing range.

A few remarks on buying such a gauge:

*NAPA sells a few such gauges, from about $15 to $30.  There are classier brands on the market (VDO), but I like NAPA because I can get all the related hardware at one store.

*Get a brass "T" fitting to screw into the hole where your idiot light sender now lives.  The "T" should accommodate both the tube running to the new gauge on or under your dash as well as the idiot light sender.

*NAPA sells a "hook-up" kit for the gauge.  Eschew same because it comes with a plastic capillary tube and what you want it 1/8" copper.  Buy the necessary additional fittings to make the copper work for you, and when you install it, create a generous loop in the copper to allow for flexing between the engine and car body.  Nylon cable ties make nice routing attachments for the line.  Route away from the exhaust pipe.

The volume of response to the b.s. piece was gratifying, in particular the two informative letters that appeared in the March NINES.  They in turn caused me to dig a little deeper into the subject.

Mr. Fowler is right on in stating the hard life of the b.s. bearing.  Having driven two V-4s a mile or so minus all the teeth on their b.s. gears, I'm here to tell you you can feel the undamped vibration through the car.  (If you find yourself in that unhappy situation, drive by your temperature gauge.  Without a working fan belt, you have NO water pump and can quickly heat-damage your engine.)  Naturally, said vibration is what the b.s. bearings have to deal with during their often all-too-short lives.  But is their demise caused primarily by fatigue, as Mr. Fowler posits?  In Automotive Engine Rebuilding by James G. Hughes (1984), Mr. Hughes lists a number of causes for engine bearing failure.  Under "Fatigue (lining break out)" he says its..."main cause is load concentration on one section of the surface rather than overall."  If, as Mr. Harris points out, overtight fan belts are a major contributing factor in b.s. bearing failure, then Mr. Fowler is right on the money vis-a-vis the above definition.  Another interesting mode of failure Mr. Hughes points out might have definite application to the b.s. bearings; Cavitiation erosion is caused when the "oil film (UNDER VIBRATION) pulls out lining material grain by grain."  (Caps mine, () Mr. Hughes).  Perhaps b.s. bearing failure is a combination of some of the previously mentioned forces.  We may never be 100% certain as to the exact cause(s) of failure because by the time you oil pressure drops dramatically or your b.s. gear fails, all such bearing failure physically looks pretty much the same.

Mr. Fowler also pointed out that the manual bearing test I described in the January NINES doesn't always show a bearing that is in the process of failing.  That is why I preceded that "test description" with the word "occasionally", and went on to say that such a bearing could be within a gnat's ass of failure and your hand/eye an oil pressure gauge is your best insurance against being caught with your V-4 pants down.

One thing I learned from Mr. Hughes book that might be of general interest is the phenomenon of corrosion failure of engine bearings.  It can be caused by a variety of contaminants in the oil.  One such source of corrosion is the fatty acids contained in some brands of "top oil".  If you're using or thinking of using top oil or a top oil lubrication system as an expedient to avoid the cost of a new set of no-lead cylinder heads, you might want to look a bit more closely.  In some of the vintage/classic car magazines such oil are being advertised as a replacement for the action of lead in gasoline.