AN296

SLEEVES FOR 2-STROKES

I am in the process of having sleeves manufactured for my SAAB two-cycle engines. The reason for this project is so that I can continue driving my 95 andn 96. The SAAB company is obviously not interested in keeping these old ones on the road, so I must look ahead.

SAAB lists for standard size pistons and four different oversizes. This is simply too many sizes to contend with for many reasons. I think a very good solution is to install sleeves and use one size piston. Then when necessary one can install new sleeves and pistons.

At this point you are probably thinking about the task of accurately cutting the ports. That can be done without too much difficulty using sophisticated machines. However it is expensive unless the quantity is sufficient for mass production.

I am having enough produced to get a reasonable price. Are there other two-cycle SAAB owners who would like a sleeved engine?

UPDATE

NESC contacted the author of this article to gain additional information as to the success of this sleeving. We did receive a response that he did not follow thru with this idea, the main reason was the lack of additional parts required to perform this job.

3-17-90