AN302

V-4 TIE ROD REPLACEMENT

Here is a method I have found useful for freeing the tapered joint of the tie rod ends on V-4's using no tool special tools and with no damage to the grease boot.

1. Jack the car and remove the wheel on the offending side.

2. Loosen the jam nut on the tie rod. This is easier to do while    both ends are still held down. Just back it off 1/4 to 1/2 turn    and remember it so you an restore the alignment on the new one.

3. Remove the cotter pin and nut from the tie rod.

4. Find a short piece of heavy pipe and a small piece of heavy       plate. Place the pipe on the floor vertically with the plate on     top and center this under the rod end. Another possibility would     be a second jack.

5. Carefully lower the car, checking to make sure the stud end of    the tie rod end is going to end up solidly on the plate.

6. After you make contact, continue to lower the jack until you      transfer a couple hundred pounds of the car's weight onto the     pipe. The steering arm is probably strong enough to take the      entire weight of the car, but that is not necessary. Just a few     hundred pounds will do nicely.

7. Hold a blunt chisel or bar on the top of the steering arm near    the rod end, and wack it smartly with a heavy hammer. The    steering arm will pop loose and drop a half an inch and settle    on the pipe, leaving the rod end loose in the hole.