AN307

V-4 SPARK PLUG WIRES

If you own a V-4 in need of a new spark plug wire set, the current price at your local SAAB dealer is about $50.00. I would suggest you make your own from a universal set for a 4 cylinder engine. The only area you may run into a problem is on the #1 plug wire where it must clear the alternator. A firm called Dorcey sells accessories for motorcycles, which can be found at some auto parts stores. They sell an elbow boot for spark plugs.  A set of 2 is about $2.50 and is a good solution to the problem.

A problem I have encountered with early 2-strokes is the very long length of the coil wire. Using the 4 cylinder kit will provide you with an extra wire, which should be joined to create the longer wire needed.

If you have great problems removing the #1 spark plug because of interference with the alternator (V-4's), you need a very simple tool, SAAB P/N 88-02-167. The last time I bought one it was very inexpensive at $2.30. It's a must for every V-4 owner.