AN308

OVERHEATING CURES

If the water pump of your 96 (or other V-4) goes up even to the point of boiling over for no apparent reason, you may want to check the bypass hose. This hose goes from the top of the engine next to to the thermostate to the input of the water pump. The purpose of this  hose is to keep the pump from having to push the coolant against a dead head when the themostate is closed and the heater is off. This hose MUST have a restriction in  it, otherwise the coolant can take this route and not bother to go thru the the radiator! My problem was intermittent and it took me two months to find it. The restriction looks like a piece of tubing that has been pinched. Someone apparently thought it was a bad piece of hose and rplaced it with universal hose.