AN310

OIL PRIMING V-4 ENGINE

I'd like to relay a suggestion made ny my neighbor, for priming a rebuilt or new V-4 engine.

Remove the distributor. Place a 6mm, 1/4" drive socket and extension onto the hexagonal oil pump drive shaft. Rotate with a speed wrench or electric drill until sump oil is circulated throughout the engine prior to a sparked start attempt.

Alternately, remove the spark plugs, ground the coil high tension wire, then spin the engine using the starter, until the oil is circulated throughout the engine. Use molybdenum disulfide assembly lube during reassembling, on cams, bearings, etc, to be safe.