AN312

V-4 THOUGHTS

I remember a long article in the local paper about 5 years ago in praise of the 96. The author, poor soul, sold off his 96 after only 140K miles because of wet starting trouble. He had replaced all the electrics back to the distributor (coil, plugs, points, wires, cap, rotor, battery, starter) with no luck. I think I know what his trouble was. There is a little wire which grounds the point plate to the plate it rides on. i had a car where this wire didn't matter; it ran fine even after it came loose, but another would completely stop when it became disconnected; tricky because it didn't look disconnected. A soldering gun will solder it back, one of those pencil things won't work.

An old letter in a recent issue detailed starter replacement. It had you removing the engine mount. If I remember correctly there are two starters. My '72 has a larger one than my '73, and I think you can get the shorter one out without the engine mount needing removal. The long one does require this step.

There have been some elaborate articles detailing a "non-lead" retrofit for V-4 heads. A local mechanic tells me the problem is not heat, but lubrication. The high heat, he says, in most unleaded cars is due to the catalytic converter. He says lubrication can be restores by adding "top oil", "2-cycle oil" or other additives to the gas (4 oz. 2-cycle oil to 10 gallons of gas?). i haven't tried this and profess to know nothing. I have been adding the aftermarket "lead substitute" (without lead), but this is not cheap.