AN317

FRAME REPAIR FOR SONETT

My 1973 Sonett III is coming down for frame repair this spring.  The front clip came off recently revealing significant rust.  However, it is repairable.

Since body and frame repair is likely to be needed on the majority of older Saabs, it might be worthwhile if I submit progress reports on this project.

For starters, it is a bit difficult to clearly describe the Sonett frame/underbody.  Here goes:  It is a welded steel frame, of unibody design.  The passenger compartment consists of two side rails, a continuous floor pan, and two bulkheads, one forward, one aft.  The forward bulkhead is also a firewall, and the aft bulkhead serves as a crash shield for the gas tank.  A roll bar is installed, which is necessary to support the fiberglass roof.

A forward subframe supports the  engine/transmission, and transfers load to the front suspension. Two vertical panels, which could be called inner fenders, add strength to the subframe, and also protect the engine from dirt and spray kicked up tires.

A rear subframe transfers load to the rear suspension and supports the rear bumper and luggage compartment.

Bear in mind that the fiberglass clips, front and back, are lightly attached with pop rivets and screws. Clearly these fiberglass parts are designed to support themselves and not much else.  They do not contribute much to the basic strength of the Sonett frame.

Since this is a car and not an airplane, all the loads must be somehow transferred to the tires.  Loads include the weight of the engine/drivetrain, body and interior, frame and suspension, gas tank and gasoline, luggage, and of course the passengers.

There are also dynamic loads, which exist when the car is moving.  The body will generate air loads due to wind resistance and side winds.  Acceleration loads are present when stopping, starting, cornering, and driving bumpy roads.

The purpose of the steel underframe is to transfer these loads to the four tires, and to protect the passengers in a crash.  Resin reinforced fiberglass body parts are not used to carry loads because a steady load will cause the material to creep or sag at this thickness.  You could increase the thickness of the fiberglass parts to overcome creep, but the car would be much heavier and also more expensive.

My Sonett has rust damage on the side rails, floor pan, and also

AN317

on the front subframe between the suspension column and the front bulkhead.  The rear subframe has rust damage on both inner fenders, near to the shock absorber mount.  This looks like the result of tire spray, which has worn away the paint and undercoat on this surface and exposed steel to water and air.

Since I want to learn how to weld, I won't be too concerned about the time this project takes.  But I want the finishes frame to be strong and safe, and to look good as well.

I should soon know more about the options for repair.  For instance, whether new side rails can be purchased or is they must be fabricated.