AN319

SONETT AIR CLEANER ON A WEBER

You can use the original Sonett air cleaner on a Motor Sport Service carb (MSS #379011) and still clear the hood.

Cut off the round flange that fits over the original throat of a Solex carb. File clean. You can leave 1/16" or so, it isn't critical.

The crank breather tube has to be bent where it hits the carb, and a little filing is necessary.

Get a rubber toilet gasket at a local hardware store and trim it down in height. it should fit perfectly around the throat of the MSS carb.

Drill a hole through the top of the air cleaner lined up with the carb bolt brace. Don't drill too far back. Use a slotted shallow head bolt to fasten the assembly to the carb.

The rear mounts in the normal fashion.