AN234

FORD V-6 PARTS FOR YOUR V-4 ENGINE

V-4 valve trains suffer wear and aging the same as any other part of the engine but are usually the LAST to be repaired because they seldom fail catastrophically. Grooves wear into the shafts and the inside of the rocker arms get egg shaped allowing the arms to wobble before they start to open the valves. Consequently the valves do not start to open as far as they should, the system is noisy and almost impossible to adjust properly.

Your local Ford dealer to the rescue! Replacement parts for the Mustang V-6 either are a direct interchange (rocker arms) or an easy modification (shafts) and are considerably less expensive than SAAB parts.

The V-6 shaft must be cut to the same length as the V-4 (200mm) with a hacksaw. Note that there is an oil plug in the ends of the shafts. Note also that the holes in the V-6 shaft are not drilled symmetrically. That is, one end of the V-6 shafts has the holes drilled exactly the same as the V-4, the other does not. Cut off the end that does not, please.

Now you must plug the end of the V-6 shaft. Two methods work equally well.

1. Machine the shaft to accept the oil plug. Tap the plug out of    the cut off end and tap it into the end you just machined in the    V-6 shaft.

2. Tap threads into the end of the shaft and put in a bolt and    washer. Install the washer and bolt and tighten. now drill out    the hole for the roll pin. Drill right through the bolt you just    installed. Now the pin will retain the bolt and will hold the    spring washer as well. Before you disassemble the rocker arm    assembly take note of the way the roll pin and the spring washer    are assembled. Put them back the same way when you reassemble.

Torque the mounting bolts to 32 ft. lbs.. set the valves to .014 (intake) and .016" (exhaust), put some new gaskets on the rocker arm covers and you are done. you should have a quit running V-4 that just picked up a couple more horsepower because the valve are opening WHEN they are supposed to (not late) and AS FAR as they supposed to.

Part Numbers for the FORD parts:

Rocker Arms      E6TZ-6564A

Rocker Shafts    D2RY-6563A