AN328

VINTAGE RACING SAABS

1960 PHOENIX SAAB

This small bore sports racer was dubbed the Phoenix, because, like the mythical bird, it rose from its own ashes.

The car first appeared at the Pomona sports car races in 1960.  At that time it had a 750cc Merc outboard engine.  It also had a habit of handgrenading the engines so the clever owner turned to SAAB power.

There were other problems; the low hood defied the common engine forward-of-the-axle attitude of normal SAABs, so he decided to turn it end for end and run the little mill backwards (try that with your V4!), but this move netted him a raft of new problems.

After one more event at Tucson in 1961 and a brief slalom stint, the project was sidelined.

I found the car in 1979 dumped in a parking lot.  The owner of the lot gladly accepted my offer to take the eyesore away.  In 1984, after a difficult 4-1/2 year restoration, the car hit the asphalt of Riverside and Willow Springs.  In 1986 and 1987, it won the Vintage Auto Racing Association class GMP championship.

I received much expert assistance from Bud Clarke of J and B Imports in Orange, California, Roger Vandewalker and Jeff Whitley.  Bud was particularly helpful since he owns one of the two SAAB Quantum sports racers stateside and his partner Jay has the other.

The Phoenix currently has a 1967 oil injected 850cc Monte Carlo engine built by Bud.  The engine is only slightly breathed on, and other than a factory design racing exhaust, Allison ignition, 7 pound flywheel, trick crank and distributor gears to permit the backward running, it can be called stock.

It uses the original suspension (long ago drilled for lightness), a V-4 gearbox (to get the nice 4.88 gears) and original, but modified brake drums.

The secret of its success is reliability, a low weight of 972 pounds, and SAAB front wheel drive agility that has many Lotus 7, Sprite and AC Bristol drivers muttering to themselves.  The car is quick to 60mph from a dead stop, around 9 seconds, and can top 112 mph on Riverside's long straight, turning 6200rpm.

The Phoenix is actively campaigned in California, and is only limited by my abilities.  Before you volunteer to drive, consider that the shift pattern is also reverse, and a bit like stirring soup as the shifter is cable operated.

I have raced on and off since 1955 in many types of race cars, but this little car really gets me going.  Maybe it's the reverbs off the mountainside as the little engine snarls its defiance at large displacement cars, maybe it's the smell of the exhaust, I don't know.  I prefer racing a "corn popper"...I wouldn't have it any other way.

Two strokes forever!

VINTAGE SAAB RACING GROUP

Pictured here are the cars of the Vintage SAAB Racing Group at the recent Walter Mitty Challenge vintage races held at Road Atlanta.

Since the feature race for this event was a one hour enduro open to cars over 1300cc, the Sonett II was outfitted with a V-4, which worked out well since the two-stroke killer motor isn't finished yet.  I had to use the hood from my street car in order to clear the carb, hence the yellow hood on a red car.

The car in the center is a Bandini SAAB, owned and raced by Cecel Stockard, a semi-retired 72-year-old attorney from Atlanta.  He's raced this car for over fifteen years with a twin carb 850cc SAAB Non-oil injected engine.

The third car is my Quantum Formula S.

We all did well on Saturday, The Quantum started last of 46 cars in its race group and finished 33rd overall, third in class.  The Bandini had a terrific duel with an Aston Martin DB-2 and managed to hold him off at the finish.  The enduro results weren't known when I left on Sunday; seems no one bothered to tell the Timing & Scoring people about the two mandatory pit stops.

Cecil's Bandini had minor problems on Sunday, but finished the race after a brief pit stop.  During my race, there was a turn one melee on the first lap, cars spinning everywhere.  I was forced off the track in the Quantum and stray tires from the former tire wall kept me out of the guardrail.  The former tire wall kept me out of the guardrail.  The off-track excursion damaged the shift limkage, and a couple of laps after I got going again, the linkage came apart.

Our 93 vintage racer is almost finished and will be at Road Atlanta for the vintage race in August.  There will be another enduro that weekend, this time with separate races for small bore and large bore cars.

It doesn't look like I'll make it to the convention, however, the Vintage SAAB Racing Group will be represented by Tom Cox who should have one of his Quantum Formula S cars ready.

JABRO-SAAB

In the late 1950s, H-Modified was the experimental small bore sports racing class, similar to today's D-Sports Racing.  The engine size limit was 850cc, and the cars were often homebuilt.

The Jabro-SAAB was not unlike many small engines purpose built racers of today, a tubular frame (similar to a birdcage Maserati) with a fiberglass body, sold in kit form.  It differed from its Trollhattan heritage by having a conventional front engine-rear drive configuration. The Crossley engine was also used as the Jabro powerplant.  The car got its name from one if its designers, James Broadwell.  Ed Alsbury was the other.

Charles Hayes of South Bend, Indiana, has a 1959 Jabro-SAAB that he is restoring for vintage racing.  It is powered by a 750cc SAAB three-cylinder, two-stroke engine, driven through an Austin Healy Sprite transmission to a Halibrand quick change rear end.

Hayes expects to be competing at Mid-Ohio, Line Rock, Road America, and Pittsburgh Vintage races this summer.

HOMEBUILT SPORTS CAR

The car pictured (above) is a sports car I built from the remains of a 1967 96.  I call it "SABER 7" because it's a cross between a SAAB and a Berkeley, and it took seven years to build.

It started in 1976 when Gordon Rado and I were Mechanical Engineering students at California Polytechnic State University at San Luis Obisbo.  We were required to do a Senior Project and decided to work together to design and build a sports car with low initial and operating  costs, good fuel economy and light weight without sacrificing performance or safety.  The design project entailed designing a tubular frame and mathematically predicting its beam strength and torsional rigidity, constructing the frame, and testing the completed chassis to determine the proximity of its torsional rigidity to predicted values.

I stumbled upon a fiberglass shell from a 1960 Berkeley for $30 and used this as the basis for the body.  We had decided upon a front-wheel drive configuration, but our choice of powerplants was quite limited by size and weight restrictions in addition to the financial resources of unemployed college students.  Although we considered using a motorcycle engine, I came upon a forlorn 1967 96 in a field and towed it home in exchange for $250.  The 850cc 2-stroke would work just fine.  This was my first experience with a SAAB, but I was impressed enough to buy four more in the next couple of years.

We designed a tubular frame using 1" square steel tubing and incorporating the SAAB's floorpan to simplify proper alignment and mounting of the suspension members.  The wheelbase was shortened from the original 98" to 80".  The chassis was rolling within two months, and the senior project was completed one month early.

Unfortunately, subsequent work on the car slowed to a crawl as my engineering career accelerated, and the car patiently followed along as I relocated to Lompoc, Bakersfield, Newport beach, Houston, and then to Salt Lake City, where it was completed.  Recent moves have taken it to Ohio and back to California.

The chassis was driveable seven months after construction began, and it made numerous clandestine springs through the neighborhood without a hint of bodywork.  This was my first experience at fiberglass, and may well be my last.  I finally set aside the sandpaper in the fall of 1982, and introduced myself to the fine art of autobody painting with a 1/2 horsepower air compressor; i.e., spray for one minute, wait on air pressure for the next ten.  Fortunately, I completed the task before the winter snows arrived.

The Saber 7 was finally completed and licensed in March 1983.  It has cost $1200 and over 1000 hours to build.  Luckily, it received same insurance rates as a SAAB sedan, and at that time cost only $105 per year.

During the first year I won 2nd place in the Utah Region SAAB Solo II for the A/Modified class, and my wife did the same in the Ladies division.  It was gratifying to be competitive with a homebuilt, street-legal car in a class where all of my competitors towed their cars to the track.

The car weighs 1275 lb. and I'm running 195/60-14 Goodyear Eagle GTs on specially made 6" X 14" steel rims.