AN329

V-4 PERFORMANCE TIPS

Performance is a relative thing.  What do you want the car to do?  I can make your 96 so it will do 120, your Sonett 130.  Given the 65 mph speed limit are these speeds realistic?  Or do you want to suck the doors off any of a dozen turdbox turbos from a stoplight?  Everyone has to decide what level of performance they  want and 1) decide if that is possible from their Saab, and 2) decide if they are prepared for the cost of getting there.  When I had my SAAB-FIAT-CITROEN dealership.  I had a sign over the trophy case in the showroom:  "SPEED COSTS MONEY--HOW FAST DO YOU WANT TO GO?"

The Saab/Ford V4 is in a rather "cooking" state of tune so a good bit can be done with it, and the extraction of horsepower boils down to what you can do EXTERNALLY and what you have to do INTERNALLY to the engine.  In either case, you shouldn't even CONSIDER performance mods unless the engine AND the transaxle have been recently rebuilt or you intend to do it as you make the performance modifications.

EXTERNAL PERFORMANCE IMPROVERS:

Carburetion is an area that probably needs attention anyhow as the old Solex and FoMoCo "Vergassers" are getting ancient, and are probably warped out of shape by age, heat and heavy handed shade-tree wrenches.  The Weber 34 ICH is a very good replacement although it is not a ten minute job to install it.  The throttle linkage has to be revised, the throttle advance rod for the choke linkage must be repositioned to clear the power brake hose ('69 and later 95/96s only), the air cleaner must be modified and an electric wire run from the shutoff valve on the Weber to the positive side of the ignition coil.  Once all this is done and the carb adjusted, the engine picks up 4 or 5 horsepower because it is slightly larger than the originals and lets a little stronger fuel/air mix into the cylinders.  These come with either no choke or a manual choke.  Buy the latter.  The Ford engine is cold blooded and needs the feature.

Part number for the Weber 341CH carb with manual choke is 15290-027.

Exhaust comes next and is best done after you do the carb swap so you don't have to mess with a carburetor twice.  The exhaust shown is an extractor system and will lean down the mixture to the cylinders too much unless you increase the size of the main jet in the carburetor.  The 341CH Weber is usually OK in this area, but you should always check the color of the spark plugs and the exhaust for the nice, even charcoal grey that tells you you are just right.

You can build the header portion of the extractor exhaust system and then run it back into your stock system if you wish.  It will be a bit more quiet than with the glasspack muffler but will be down just a little on power by comparison.

Any good muffler shop should be able to build you this system for $100-125.  Power will improve by about 5 hp with the exhaust alone, or about 12 hp with the Weber carb.

Don't overlook the Ignition as it has hidden power lurking inside its mysterious little body.  First, rebuild it (See April '76 newsletter) and set the advance curve to the specifications shown for the 1969 Bosche 0-231-146-073 distributor (see Saab Service Manual Section 3, page 342-11).  Modify the unit so ALL the advance is IN by 1400 distributor (2800 engine) RPM.

If you are tired of changing ignition points every 4-6000 miles, you might want to consider an Allision optical firing system which eliminates the mechanical points of the standard distributor.

This system won't add horsepower but does add reliability and saves a lot of screwing around with points, dwell, etc.  You set it once and thats it.  Set your timing to 6-8 degrees before top dead center and you can figure you gained another 2-3 horsepower.

NOTE: Proper dynamic ignition timing for the Saab V4

can ONLY be done while the engine is at CRANKING

SPEED! Look at the advance curve-proper idle speed

of 1000 rpm shows several degrees of advance already

in.  If you set it at idle you will find you just

retarded the spark about 9 degrees.  Pull off all

the plug wires except #1, hook the timing light to that

wire, crank the engine over and adjust the timing.

With these external mods completed you have picked up about 15 very noticeable horsepower and will like your Saab a lot better already.

INTERNAL PERFORMANCE IMPROVEMENTS:

The BIG power gains come from a combination of external and internal modifications.  You must do a full tear down, precise overhaul and a thorough balance job on the reciprocating parts of the engine.  Without the overhaul, the engine will come unglued with attendant VERY expensive noises, and without the balancing you won't realize the full potential of your performance modifications.

I have covered the overhaul of the V4 (see Aug 84, June 85 and May 88 newsletters) so I won't go into that again.  We just apply the old hot rodders acronym CCC (cams, carbs and compression).  Since wither the 1500 or the 1700 can be used, suffice to say that the 1500 with 9+ compression is high enough, given todays gasoline octane ratings.  The 1700 can have .030" milled off the heads to squeeze things a little tighter than the engine's stock 8 to 1 compression.  Don't mill more than .030" off the heads or you have a miss-match between the heads and the intake manifold.  In either case, you will probably have to use premium fuel to prevent ping under load.  That about it for compression.

Carburetion calls for a two barrel intake manifold and a 2 barrel weber carburetor.  A new Weber 32/36 DGV carburetor is a good choice and will set you back something like $175 or if you have more time for tinkering than money, you can hit the wrecking yards for a Holley Weber 5200 carb from a Capri, Pinto or Omni/Horizon.  The 5200 is very nearly the same as the 32/36 DGV, by the way but has more smog junk attached, most of which has to be trashed and some of the openings plugged.  Neither are direct bolt-on-and-go conversions so you will have to modify linkages, add a manual choke, and adapt an air cleaner, as well as going through the jetting to make it compatible with your engine.

Any good cam grinder can regrind your Saab cam to Iskenderian regrind specs.  Isky shows two grinds for the Saab/Ford V4, the F4 and the F66.  Specs are as follows:

Intake		Exhaust		Lift   Duration

F4	19-61 degr.	61-19 degr.	.425"  260 degr.

F66	21-63 degr.	63-21 degr.	.448"  264 degr.

The F4 produces more torque and is probably best for a 95/96.  The F66 produces more horsepower but not as much in the lower RPM ranges, so it is my preference for a Sonett.  Isky's light keepers and retainers and 2-spring valve spring sets are very worthwhile.

New cam followers are a MUST as are new cam and balance shaft bearings, of course.

A couple other things you must do during this rebuild is to replace the timing gear set, and rebuild the rocker arm assemblies (see May 88 Newsletter).  You have the front cover off so check the area where the water pump is located and see if the rear cover of the pump is all chewed up and eroded.  If so the cover must be replaced,  And press out that fanshaft bearing and replace it while you're at it, as well as the seal in the cover for the balance shaft.

Some other areas need attention.  The engine block needs to be tanked to clean out the rust and scale inside the cooling system.  The V6 oil pump, a new water pump all new hoses are necessary.  The radiator must be taken apart and rodded out, repaired and painted by a good radiator shop.  The flywheel needs to be lightened (See June 85 Newsletter) and, as I mentioned earlier, the engines recip parts balanced.

The radiator needs to be the late type (1969 and later cross-flow) or a Sonett or a 99 modified to fit.  The modified engine will produce a lot more horsepower and horsepower is HEAT, so you have to be able to dissipate the heat with the cooling system.  Don't go cheap here.  If you fry that expensive engine...

In final form you can have a VERY satisfying street engine in the Saab/Ford V4.  The stock 73 horsepower can be raise the 85-88 with external mods and to 110-120 with the addition of the internal mods.  Mileage will probably be just as good (better on a long run) as stock and reliability a LOT better.  Costs can run from several hundred for external only most to $3000 or more for a full house unit.  And we haven't even mentioned turbos.

So, as allay, you pays your money and you takes your choice, from mild to wild, speed still costs money.  How fast do you want to go?

THE MAGIC OF GEAR RATIOS

One of the way to performance is through properly chosen gears in the transaxle.  Back in the days when Saab was running V4s in international rallies, the Sport and Rally catalog listed a number of close ratio gears and final drives that were available.  Nowadays about the only selection we have is Sonett gears (final drive 4.67 to 1), 95/96 V4 gears (final drive 4.88 to 1) and 2-cycle gears (final drive usually 5.43 to 1).  When I was serious about autocross racing, I had one of each in the shop for the Sonett V4 I was racing (see title picture, this article).  Short courses dictated use of the 5.43 gears which gave a stump puller 1st, but explosive acceleration out of the corners in 2nd and 3rd.  Longer courses, the other gearboxes and a varying diameter of racing tires.  As I say, I was serious about it, convinced that racing on Sunday helped sell cars on Monday, and we won a TON of trophies, often against cars we had no business beating.

Smart racers--on or off the street--have always known the value of the right gears for the type of racing and/or the particular race course. This is worth some contemplation too, as you search for more performance.

FREE POWER!

I once helped a good friend build a KILLER engine that he subsequently put into his Saab 95.  He drove it a while and then told me how disappointed he was with the car's performance.  I drive it with him and agreed.  We checked the compression, the timing, etc.  All were right.  I took a look in the back and asked him what all that "stuff" was.  We unloaded about 400 pounds of his stuff. Then I sent him out by himself to test drive it and he came back with a grim that extended around his head.  "I have never driven a Saab this fast!"  he said.

Weight is the great enemy.  Take out all the "stuff" that doesn't absolutely HAVE to be in the car.  All the junk under the seats, in the back seat, in the trunk.  PRESTO!  50 pounds lighter right there!  What else can go?  Trunk mat, floor mats, back seat, sound proofing--how bad do you want to go fast?  I'd always opt for lighter weight instead of more horsepower, if the new performance increase for the car was the same.  Why?  Because the car will also HANDLE better.  The power you gain this way is FREE.  Don't overlook it.