AN333

BACK PRESSURE CRITICAL TO MODIFIED TWO-STROKES

Just recently obtained my second Sonett, a '74, so thank for all the tips in the May '88 newsletter. The valve train tips will be useful for any upcoming valve work.

I usually agree with Jack Ashcraft's SAAB tips, but must disagree about the 2-stroke exhaust. He may be right if the car has a stock engine (my Sonett II never has while I've had it), but if the ports have been changed or it's otherwise tuned up, exhaust back pressure is critical.

I've done extensive reading, talking to motorcycle people and experimentation with my car (Stage 3 tune). Too little back pressure appears to rob high end power and is reputed to overheat pistons. Too much back pressure robs power throughout and definitely burns pistons.

I tried putting glass pack mufflers on, but only get good sound and less power. A nice clean stock Sonett rear muffler with stock diameter pipes from the resonator (my resonator is modified per Stage 3 instructions) have been my best solution for reliability, power and noise control.

All the literature I've read is adamant about the criticality of matching your front resonator length and volume to the ports sizes and timing. Exhaust outlet from the resonator is equally critical. The two-cycle works by setting up standard waves of high and low pressure in the exhaust system. These alternately scavenge the exhaust gases from the combustion chamber, and a little raw fuel, too, then stuff the raw fuel back in through the exhaust port just before it closes. Getting the system wrong will destroy the resonance of the system, and the performance of the engine. It may also make it run too hot or too lean and wreck it. Getting it right makes all worthwhile, and a treat to drive.