AN334

MISPRINT IN CHILTON'S MANUAL

Be advised that a very serious misprint appears on page 40 of CHILTON"S Repair and Tune Up Guide for SAAB (1960-70). The section relates to rebuilding the four stroke V-$ engine.

It states:

"39. Install the intake manifold. Tighten the bolts and nuts in two stages, to the correct torque:

Stage 1:   Bolts  2.9-58 ft lbs

Nuts   2.2-36 ft lbs

Stage 2:   Bolts   16-21 ft lbs

Nuts    11-13 ft lbs"

The CORRECT TORQUE SPECIFICATION under Stage 1 should be:

Bolts  2.9-5.8  ft lbs

Nuts   2.2-3.6  ft lbs

By following these directions, I overtighten all the inlet manifold bolts and had one break. It took a couple of days to correct the problem.