AN336

97 SPEAKER INSTALLATION

There is a very simple way to install speakers in your Sonett.

Remove the seats, carpet under the seats, front carpet and floor boards ( good time to check for rust, clean things up).

Feel the upholstery on the front of the gas tank, just to the left of the rear window release on a Sonett III, same area on the Sonett II and V-4. There is a "hole" there that is perfect for a standard 5-1/4" round speaker. The chamber around it works far better than the fiberglass in the rear, and won't "block" the sound when items are placed in the back. There are also holes (the same size) for accessing your speaker wire runs down lower.

Gently peel back the material enough for access. You can re-glue it with contact cement, 3M yellow weather stripping glue in a tube, or a spray such as 3M "33" glue which sprays in a tight pattern.

Now to the front. You don't need to cut a hole in your door. Inspect the carpeted kick area just in front of the door. Peel back the glued down carpet from the bottom and there. Ditto on the other side. Use the lower set of holes as the fuse block covers most of the upper one on the driver's side. You can mount a 4-1/2 speaker there or enlarge the hole with a metal cutting jigsaw and mount matching speakers to the rear units.

Both front and rear speaker locations require just a drill for mounting the speakers, and a razor knife for cutting the holes open. Make an "X" in the material starting from the center, then trim back in a circle. Glue back any loose material, run your wires, put it all back together and crank up the tunes.

By the way, the old dash speaker works great for a CB radio.

If you're installing an amp/equalizer, you can hang it under the glovebox if so desired. Another area is under the dash, just left of the steering column. That depends on the size of the unit, and if you desire to keep you passengers' little hands off of it.