AN337

SONETT OVERFLOW TANK

Save yourself summer heating troubles by installing one of these simple regeneration tanks on your Sonett. At $3-5.00 they are one of the last great auto bargains. Don't use the 14 P.S.I. radiator cap from the kit, just the rubber seal at of that cap. Its the key to making this thing regenerate water out of the plastic tank on back into the expansion tank of the Sonett. Mount the plastic tank on one of the existing screws of the heater box, hook up  the plastic hose, switch the rubber seal from the cap in the kit to the standard Sonett radiator cap, and the job is done. Keep the plastic tank about 3/4 full of regular radiator coolant.