AN338

REBUILDING TWO-STROKE WATER PUMPS

I have a solution for water pump rebuilding on the Sonett II/Monte Carlo 850 2-cycle engine.

I disassembled a spare worn pump; the bearing was shot, seals were okay. I took the bearing to a bearing supply house with the vague hope of finding some sort of match. Also took along a disassembled pump from my '51 Ford 6-cylinder truck, another no longer available part.

The bearing man took 30 seconds to put two bearings in my hands. It turns out at least 50% of water pump bearings use the same basic bearing, including the '67 SAAB and '51 Ford. There was no manufacturer name on the box, but the part number was 885158.

All you have to do is take the water pump to a machine shop and have them cut the shaft to size and grind it down to the right diameter on the ends. It cost me about $25 for the two bearings and $20 for machining.

I'm having to re-use the old seals, so I've soaked those in rubber restorative liquid (Armor All or equivalent).

So don't throw away those worn, wobbly water pumps. Disassembling them, save the seals, and you can rebuild them.