AN35

MORE V-4 TIPS

On the V-4 the front cover seal can be replaced perfectly with a Chicago Rawhide seal # 13985, and the rear main seal can be replaced with Chicago Rawhide # 23632. You may be able to get these thru your NAPA store.

When overhauling V-4 engines, a top end gasket set is all that is needed. Silicone form a gasket works fine for the front plate, front cover, oil pan. I then make gaskets from gasket material for the oil pump , pickup, fuel pump. I've also used Silicone ONLY for the the valve covers- it makes a permanent gasket by running a bead around (clean) valve cover gasket groove, let set 24 hours, and from then on when the tappets are due for setting, pop the covers off, set tappets, install coversn and no seeps.