AN353

V-4 HOSE HINTS

These special size, dealer-imported radiator hoses cost a lot and don't always fir well, so I look for American substitutes more available.

The 5-inch hose coming out of the waterpump outlet (this hose is 1" ID) can be cut from a Gates hose #20782. In fact, the curve fits better, and you can get two hoses for a V-4 from that one part!

Gates hose #21257 is a great replacement for the curved heater hose which loops back to the heater from itself. It fits perfectly if you cut part of the Gates hose. This piece of excess can be used to replace a nearby hose perfectly.

The top hose on the radiator can be replaced by Gates #26403. I've heard that the U-shaped on under the radiator can be replaced by John Bull hose #913, but I haven't verified this.

Doorman MIS>118025 may work as substitute throttle linkage clips. As for the tiny "washer" holding linkage to the stepped cam, you can use J & T 0705 if you have to.